## Slide 1: Enterprise Network Design Project
Designed using Cisco Packet Tracer

## Slide 2: Project Team
Group Leader
Topology Designer
Documentation Lead
Budget Analyst
Remote Access & Security Specialist
Packet Tracer Implementation Specialist
Quality Assurance & Review Lead
LT. NKOSIYAPHANTSI – 45720185
TD. MOHAPI – 42570603
TP. KEKANA – 44158955
T. Van Wyk – 45603073
J. MASHININI – 47219815
IK. NGOBENI – 43019080
KK. KHANYE – 45919348

## Slide 3: Project Overview
As part of an office expansion initiative, this project involved designing a low-cost, scalable enterprise network for a newly constructed office building. The network supports both wired and wireless access for employees and guests across multiple departments.
Key Features:
Supports desktops, laptops, and mobile devices.
Centralized server room with DHCP, DNS, NAT, and intranet services.
Secure Wi-Fi for staff; isolated guest access.
Seamless inter-office communication & centralized storage.
Remote access for hybrid work via VPN/SSH.
Fully simulated and configured in Cisco Packet Tracer.

## Slide 4: Network Topology
Topology Type: A hybrid ring-extended star topology was used. Each office operates on a star structure, while all switches are interconnected via a hierarchical inter-router backbone, with 6 routers forming a ring for redundancy.
Structure Summary:
Offices connect to dedicated switches (max 8 PCs per switch).
Switches are linked to routers in hierarchical layers.
Router 6 serves as the backbone router and connects to the file server.
This design supports scalability, redundancy, and clear core-distribution-access layering.

## Slide 5: Detailed Breakdown of Network Components
Offices and PCs
13 Offices (Office 1 -13 includes the technicians office)
Each office has 4 PCs
Each group of office connect to dedicated switch
Switch 1 -Office 1 & 2
Switch 2 -Office 3 & 4
Switch 3- Technician Office
Switch 4 -Office 5 &6
Switch 5 -Office 7 & 8
Switch 6 -Office 9 & 10
Switch 7 -Office 11 & 12
Routers and connectivity
Router 1 – File server
Router 2 – switch 1 & 2
Router 3 – switch 3
Router 4 – switch 4 & 5
Router 5 – switch 6 & 7
Router 6 – Backbone + entry

## Slide 6: IP Addressing Schema
Office | IP range | Getaway
1 & 2 | 192.168.1.2 – 192.168.1.9 | 192.168.1.1
3 & 4 | 192.168.2.2 – 192.168.2.9 | 192.168.2.1
5 & 6 | 192.168.3.2 – 192.168.3.9 | 192.168.3.1
7 & 8 | 192.168.4.2 – 192.168.4.9 | 192.168.4.1
9 & 10 | 192.168.6.2 – 192.168.6.9 | 192.168.6.1
11 & 12 | 192.168.7.2 – 192.168.7.9 | 192.168.7.1
Technician Office | 192.168.5.2 – 192.168.5.3 | 192.168.5.1
Server Room | 192.168.5.5 | 192.168.5.1
Reception room | 192.168.8.2 -192.168.8.3 | 192.168.8.1
Reception printer | 192.168.8.4 | 192.168.8.1
Open floor printer | 192.168.10.2 – 192.168.10.6 | 192.168.10.1
BoardRoom PC | 192.168.8.5 | 192.168.8.1

## Slide 7: Network Design Consideration
Section 1: Reception
2 Wired Access Points (Staff PCs)
1 Network Printer (Accessible enterprise-wide)
Wi-Fi Access:
  Staff: 2–4 devices each (personal/work)
  Guests: Limited internet access only, isolated from LAN
Section 2: Server Room
Hosts: Core Routers, Switches & Servers (DHCP, DNS, NAT, Storage).
No General Staff Access (Technicians only).
Internet Gateway Point; internal traffic bypasses unless necessary.

## Slide 8: Network Design Consideration(cont…)
Section 3: Technician Room
2 Wired Workstations + 2 Wired Task Aps.
4 Wired Test Ports (For equipment testing).
Wi-Fi: 8 Devices per Technician.
Dedicated Line to Server Room (for maintenance/troubleshooting).
Section 4: Staff Offices
Integrated Network Communication & Sharing.
Wi-Fi Access: 2–4 personal/work devices per user.
Connectivity via intermediate switches to core.
Supports inter-office comms, file & printer sharing.
Centralized data access across all offices.

## Slide 9: Network Design Consideration(cont…)
Section 5: Remote Access
Secure connections via VPN / SSH.
Remote access to internal resources (files, intranet).
Managed via central server infrastructure (enables hybrid work).
Fully supports hybrid work environments.
Section 6: Store Room
LAN-Isolated from enterprise network.
Internet Access Enabled.
No internal communication needed.
No switch or AP installed in this room.
Upper-left corner office of the building.

## Slide 10: Network Design
Tool Used:
Designed using Cisco Packet Tracer v9.0.0
Design Objectives:
Meet earlier design considerations through:
  Strategic hardware layout.
  Proper IP addressing (192.168.x.x /24 per zone).
  Efficient device interconnectivity.
  Secure & organized inter-office communication.
Key Features:
Secure & Organized Communication across all office sections.
Centralized Services hosted in a secure server room.
Reliable Internet Access for all network zones.
Cost-Effective & Scalable Design principles applied.
Remote Connectivity:
Supports VPN & SSH for hybrid and off-site staff.
Ensures safe access to internal resources from remote locations.

## Slide 11: Reflection on Network Design
Key Challenges:
IP Address Allocation across multiple subnets while ensuring full connectivity.
Configuring RIP routing protocols (frequent “host unreachable” errors).
Bridging theory vs practical implementation.
Packet Tracer limitations: simplified VLAN, wireless, and firewall settings.
Visual layout management becoming complex as topology grew.
Key Takeaways:
Gained hands-on skills in network design, IP planning, and troubleshooting.
Documentation should be written alongside design decisions, not after.
Importance of planning the IP schema before building the topology.
Build and test one zone at a time to isolate configuration errors.
Laid a solid foundation for future growth with advanced tools.

## Slide 12: Budget
Cost-Conscious Design Strategy:
Prioritized cost-effective solutions without sacrificing performance.
Focused on multipurpose devices (e.g., VLAN-capable switches, routers with built-in Wi-Fi).
Key Budgeting Decisions:
Avoided expensive enterprise-grade hardware.
Chose standard switches & access points suitable for expected load.
Reused existing servers and infrastructure.
Standardized device models to reduce support/training costs.

## Slide 13: Budget(continues….)
Devices | Quantity | Prices | Total
Switch | 10 | R1 700 | R17 000
Wireless router | 4 | R740 | R2 960
Modem | 1 | R450 | R450
PT routers | 6 | R3 500 | R21 000
Telephone (conference) | 1 | R2 700 | R2 700
Access Points | 87 | R1 200 | R104 400
Material Subtotal |  |  | R148 510
Labour (7 member x 2 days x R6 982/day) |  |  | R97 748
TOTAL PROJECT COST |  |  | R256 258

## Slide 14: Remote Group Work
Work Strategy:
In-person meetings for hands-on configuration & collaborative troubleshooting.
Remote work for ongoing progress and task distribution.
Tools Used:
WhatsApp Group Calls: Task planning, updates, and decision-making.
Collaboration Approach:
Tasks aligned with members’ strengths.
Rotating documentation duties to build writing skills & ensure equal contribution.

## Slide 15: Remote work reflection
Key Challenges:
Scheduling conflicts affected task coordination.
Occasional missed deadlines led to frustration.
Required thoughtful task distribution to match skills and availability.
Asynchronous communication introduced decision delays.
Positive Responses:
Maintained a supportive, team-focused environment.
Peer encouragement helped sustain morale.
Focused on collaboration over blame.
Communication & Growth:
WhatsApp was key for updates, accountability, and clarification.

## Slide 16: Conclusion
Network Design – Hybrid ring-extended star topology — 6 routers, 10 switches, 87 APs across all zones.
Requirements Met – All zones have Internet access. Wired ≥50 Mb/s, Wi-Fi ≥10 Mb/s. Machine room centralised.
Security – Guest Wi-Fi isolated. Store room excluded. Remote staff authenticated via VPN/SSH.
Budget – Total R246 258 (R148 510 hardware + R97 748 labour) — cost-effective for a 5 000 m² building.
Lessons Learned – Plan IP schema first. Build zone by zone. Document decisions as they are made.

## Slide 17: Reference
Cisco Systems. (2025). Cisco Packet Tracer 9.0.0 – Network simulation tool. Retrieved from https://www.netacad.com/courses/packet-tracer
Sejaphala, L. (2024). CMPG315 Computer Networks Study Guide. North-West University
Tanenbaum, A. S., & Wetherall, D. (2011). Computer Networks (5th ed.). Pearson Education.